## Slide 1: PAULOWNIA WOOD PLANTATION SHUTTERS Worldwide Australia – Technical Specification
PANEL SIZING (GUIDE) Minimum Width: 190 mm Height: 254 mm Maximum Width Hinged: 950 mm Fixed: 850 mm Bi‑fold track: 650 mm Sliding: 950 mm Sliding with centre stile: 1200 mm Maximum Height 3000 mm Mid‑Rails 1 required: 1500–2499 mm 2 required: 2500–3000 mm RAIL SIZES Top / Bottom: 76.2–178 mm Mid‑rail: 76.2 mm (63 / 89 / 114 louvre) 63.5 mm (76 louvre) OPTIONS Hidden hinges (frame dependent), half‑raised panels, ring pulls, locks, skylight locks, flush bolts, blackout blinds, horizontal T‑posts, tier‑on‑tier, shaped shutters (arch, circle, rake). WARRANTY 2 Years (painted or stained)
APPLICATION Interior applications in non‑wet areas. MATERIAL & BUILD Paulownia timber Lightweight construction Approx. weight: 11 kg/m² Motorisation: Available COLOURS & FINISHES Painted: 34 standard colours Stain (closed grain): 8 colours Stain (open grain): 6 colours Brushed finishes: 8 colours Custom paint colour: Available LOUVRES & STILES Louvre sizes: 63 / 76 / 89 / 114 mm Stile profiles: Beaded or Flat Stile sizes: 38.1 / 50.8 / 60 mm TILT & CONTROL Clearview tilt rod Centre tilt rod Concealed tilt rod Split control limits apply by blade size Motorised operation available

## Slide 2: BASSWOOD PLANTATION SHUTTERS Worldwide Australia – Technical Specification
PANEL SIZING (GUIDE) Minimum Width: 190 mm Height: 254 mm Maximum Width Hinged: 950 mm Fixed: 900 mm Bi‑fold track: 650 mm Sliding: 950 mm Sliding with centre stile: 1200 mm Double‑hinged overall width limits apply Maximum Height 3000 mm Mid‑Rails 1 required: 1500–2499 mm 2 required: 2500–3000 mm RAIL SIZES Top / Bottom: 76.2–178 mm Mid‑rail: 80.2 mm (63 / 89 / 114 louvre) 67.5 mm (76 louvre) OPTIONS Half‑raised panels, ring pulls, locks, skylight locks, blackout blinds, horizontal T‑posts, tier‑on‑tier. WARRANTY 2 Years (painted)
APPLICATION Interior applications in non‑wet areas. MATERIAL & BUILD Basswood timber Higher‑density timber construction Approx. weight: 14 kg/m² Motorisation: Available COLOURS & FINISHES Painted: 34 standard colours Custom paint colour: Available LOUVRES & STILES Louvre sizes: 63 / 76 / 89 / 114 mm Stile profiles: Beaded or Flat Stile sizes: 38.1 / 50.8 / 60 mm TILT & CONTROL Clearview tilt rod Centre tilt rod Concealed tilt rod Split control limits apply by blade size

## Slide 3: ASHWOOD PLANTATION SHUTTERS Worldwide Australia – Technical Specification
PANEL SIZING (GUIDE) Minimum Width: 190 mm Height: 254 mm Maximum Width Hinged: 950 mm Fixed: 850 mm Bi‑fold track: 650 mm Sliding: 950 mm Maximum Height 2400 mm Mid‑Rails Required from 1500 mm OPTIONS Half‑raised panels, ring pulls, locks, flush bolts, blackout blinds, horizontal T‑posts, tier‑on‑tier, shaped shutters. WARRANTY Refer to Worldwide warranty terms
APPLICATION Interior applications in non‑wet areas. MATERIAL & BUILD Ashwood timber High‑density construction Approx. weight: 16 kg/m² Motorisation: Available COLOURS & FINISHES Painted: 34 standard colours Stain (closed grain): 8 colours Stain (open grain): 6 colours Brushed finishes: 8 colours Custom paint colour: Available LOUVRES & STILES Louvre sizes: 63 / 76 / 89 mm Stile profile: Flat Stile sizes: 38.1 / 50.8 mm TILT & CONTROL Clearview tilt rod Centre tilt rod Concealed tilt rod

## Slide 4: POLY PLANTATION SHUTTERS Worldwide Australia – Technical Specification
PANEL SIZING (GUIDE) Minimum Width: 190 mm Height: 254 mm Maximum Width Hinged: 950 mm Fixed: 900 mm Bi‑fold track: 650 mm Sliding: 950 mm Double‑sliding: 1700 mm Maximum Height 3000 mm Mid‑Rails 1 required: 1500–2499 mm 2 required: 2500–3000 mm RAIL SIZES Top / Bottom: 76.2–150 mm Mid‑rail: 80.2 mm (63 / 89 / 114 louvre) 67.5 mm (76 louvre) OPTIONS Locks, flush bolts, blackout blinds, horizontal T‑posts, tier‑on‑tier. PVC systems utilise wooden boards and track systems where specified. WARRANTY 3 Years
APPLICATION Interior use in wet or high‑humidity areas. MATERIAL & BUILD PVC construction with reinforced blades Moisture‑resistant Approx. weight: 15 kg/m² Motorisation: Available COLOURS & FINISHES Painted: 34 standard colours Custom paint colour: Available LOUVRES & STILES Louvre sizes: 63 / 76 / 89 / 114 mm Stile profiles: Beaded or Flat Stile size: 50.8 mm TILT & CONTROL Clearview tilt rod Centre tilt rod Concealed tilt rod

## Slide 5: ALUMINIUM PLANTATION SHUTTERS Worldwide Australia – Technical Specification
PANEL SIZING (GUIDE) Minimum Width: 190 mm Height: 254 mm Maximum Width Hinged: 1200 mm Fixed: 1200 mm Bi‑fold track: 650 mm Sliding: 1200 mm Maximum Height 3000 mm RAIL SIZES Top / Bottom: 83–130 mm Mid‑rail: 80.2 mm OPTIONS Locks, flush bolts, outdoor‑rated hardware. WARRANTY Refer to Worldwide warranty terms
APPLICATION Suitable for indoor and outdoor use, including wet areas. MATERIAL & BUILD Aluminium construction High durability Approx. weight: 20 kg/m² Motorisation: Available (120°) COLOURS & FINISHES Powder‑coated: 5 standard colours Custom paint colour: Available LOUVRES & STILES Louvre size: 89 mm only Stile profile: Beaded only Stile size: 50.8 mm TILT & CONTROL Clearview tilt rod Centre & concealed tilt rods: Not available